## Slide 1: List of input files
Observation file
  crx or rnx format
  Version 2 or 3
Navigation file
  e.g., BRDC00IGS_R_20191810000_01D_MN.rnx
  One or multiple files depending on the file version
  Version 2 or 3
Precise orbit files (optional)
  .sp3 (e.g., COD0MGXFIN_20191800000_01D_05M_ORB.SP3)
  Three sequential days (one day before to one day after)
  ftp://igs.ign.fr/pub/igs/products/mgex/
Clock information file (optional)
  .CLK (e.g., COD0MGXFIN_20191810000_01D_30S_CLK.CLK)
  ftp://igs.ign.fr/pub/igs/products/mgex/
Differential code bias information file (optional)
  .BSX (e.g., CAS0MGXRAP_20191810000_01D_01D_DCB.BSX)
  ftp://ftp.cddis.eosdis.nasa.gov/gnss/products/bias/.
Ocean tide loading information (optional)
  http://holt.oso.chalmers.se/loading/
Pole tide information (optional)
  https://www.iers.org/IERS/EN/Publications/Bulletins/bulletins.html
  Bulletin B data should be saved in a text format (Bulletin_B.txt)

## Slide 2
Observation file
Navigation files
(Data folder)
input_db
epoch_array
options
Navigation, SP3, CLK, DCB, Antex, Pole tide
Read correction information files (read_files.m)
rxnav.m read_sp3.m read_clk.m read_antex.m read_DCB.m read_recDCB.m read_pole_tide_coeff.m
Create Database (create_DB.m)
crx2rnx.exe gfzrnx_win64.exe multipos.exe
Compute and apply the corrections (correction_DB.m)
apply_satDCB.m apply_recDCB.m apply_sat_pos_clk.m wind_up.m relativistic_clock_error_correction.m cal_sat_PCV.m cal_rec_PCO.m cal_rec_PCV.m cal_rec_arp.m SolidTide_comp.m OceanLoad.m PoleTide.m relativistic_range_error_correction.m
corr_DB
input_db
options
input_db
options
Run PPP_OSU (PPP_KF.m)
PPP_code_phase_KF.m or PPP_code_phase_KF_noRecDCB.m (depending on options.recDCB_ind) Adaptive_Robust_KF.m
input_db
epoch_array
Options
corr_DB
Output files in out_dir